## Slide 1: A Small-Scale Washing and Cooling Unit
Flywheel Farm, LLC Woodbury, Vermont

## Slide 2
Flywheel Farm - started 2013
Diverse: fruit, veggie, small livestock
Current acreage in production: 2; Max: 4
30% retail, 70% wholesale
8’x20’ Packhouse and Walk-in Cooler

## Slide 3
What do we want to accomplish with our Packhouse and Walk-in?
Efficient Use of Labor
Quality Produce

## Slide 4: 2013 8’ x 8’ structure using a woodshed design. No electric, no phone.
3 plastic utility sinks, salad spinner, table, floor, roof.

## Slide 5: Past Experiences/Seen on Other Farms
We disliked…
Manual dumping of H2O
Mix ‘n match basins
Bathtubs
Unreachable/lost spaces
Filling tubs with hoses
Exposure to rain/snow
Systems that require constant reconfiguration
Systems that require more than one person
We liked…
- Laundry/Utility sinks
Empty, Cleanable tabletops and floors
Lots of air-flow and light
Floors that drain
Cooler close to Packing
Cool-bots
Considering Efficiency, Ease of Use, Cleanliness

## Slide 6: 8’ x 20’ Packhouse & Cooler
COOLER
5 x 7 x 6
210 cu ft
SINKS
SALAD SPINNER
LOW DRAIN
TABLE
PACK TABLE
PHONE
ELECTRIC
INTERNET
PRESSURE TREATED DECK
HARVEST TOTE STORAGE

## Slide 8
Used the cool-bot website for design ideas
Keeping the floor level with packhouse and a continuous roofline meant a low cooler ceiling (6’).
4” Poly ISO insulation, R-23
Purchased insulated door, then cut to fit.
10,000 BTU A/C unit with Cool-Bot
Walk-In Construction

## Slide 9
Utilities
200 feet of buried wire and ethernet cable
40 Amp service with subpanel at packhouse
Packhouse becomes the main electrical and communications hub for the farm

## Slide 10: Farm-Specific Design
Wholesale Produce:
Picked to order
Primarily Greens: bunched and loose leaf
Retail Produce:
Picked weekly
Smaller volume of diverse mixed vegetables
Run by 1 person
Contains everything we need to fill orders
Limits of space match those of our acreage

## Slide 11: Designing Flow for Food Safety & Efficiency
Triple – rinse for greens
Flow
Walk-in
Cooler
PICK – RINSE – PACK – STORE - SEND

## Slide 12
Cooler Interior
Cases are easy to pack in; cooler is easy to clean out
vinyl flooring
walls and ceiling are FRP wall board
Removable, off-the-floor shelving system

## Slide 13
Separate hand- and tool-washing sink outside packhouse
Clearly marked Harvest buckets stored separately
Clearly marked ‘Compost,’ ‘Rabbit’ and ‘Trash’ bins

## Slide 14: Material & Equipment Costs
Total $ 3,700
2013 Prep Area Structure with Sinks and Fittings $ 720
2014 Prep Area Walls and Cooler Expansion $ 1,700
A/C & Cool-Bot $ 600
Electric and Phone/Internet $ 680

## Slide 15: Using the space
Forms the Center of the Farm
Only shady, out-of-the-dirt place to sit
Farm office: take orders, check messages
Where we charge batteries, scales
Water hub: where we hook up drip irrigation
Refrigerator can fit inside cooler (zone potential)
Cooler can be made freeze-proof

## Slide 16: Improving the Space
Current Issues
Becomes a magnet for tools that get only halfway back to the barn…
1) Clean up at the end of the day
2) Have a place to hang tools up
Build-up of non-refrigerated produce
1) Sell that stuff
Next Projects
Complete drainage
Add heater so cooler doesn’t freeze in winter